## Slide 1: Observation System Simulations for the GOLD Mission
Stan Solomon
High Altitude Observatory
National Center for Atmospheric Research
HAO/NCAR • 1 February 2016

## Slide 2: Outline
• The Global-scale Observations of the Limb and Disk mission
— introduction and overview
• Observations and measurement technique
• Global Modeling and airglow simulations
• Work in progress on radiative transfer effects

## Slide 3: Global-scale Observations of the Limb and Disk
Richard Eastes, PI
UCF
Bill McClintock, DPI
CU/LASP
Alan Burns, Project Scientist
HAO/NCAR

## Slide 4: GOLD Ultraviolet Imaging Spectrograph
Instrument Summary | 
Volume | 51×55×69 cm3
Mass | 33 kg
Power | 53 W
Data Rate | 3.3 Mbit/sec
• Two identical channels
• Fully independent observing modes
  – Disk images and limb scans
    - Dayside: T and O/N2
    - Nightside: O+ density
  – Stellar occultation
• Heritage
    – Cassini UVIS
    – MESSENGER MASCS
    – MAVEN IUVS
  • Deployed on a Geostationary Comsat
    — Provided by SES-GS
    — Airbus SES-14 at 47.5 W long.
    — Launch in late 2017

## Slide 5: GOLD Ultraviolet Imaging Spectrograph
Alignment Cube
1-Shot Aperture Cover
Light Shade
Solar Safety Sensor
Telescope
Slit Mech
Aperture
Scan Mechanism
Scan Mirror Visor
Detector Electronics
HVPS
Detector Assembly
Collimating Mirror

## Slide 6: Instrument Optics
Scan Mirror
Toroid Collimating Mirror
Toroidal Grating
MCP/XDL Detector
Telescope
Mirror
31º FOV
Aperture Stop
+λ
  Two independent, identical channels
  Wavelength range: 132 – 160 nm
  2-D delay line anode detectors
  Spectral resolution: 0.3 nm day, 0.5 nm night, 1.0 nm occultation
Slit
Modified Wadsworth Spectrograph w/ f/5 Spherical Telescope

## Slide 7: GOLD Measurement Technique
Daytime Far-Ultraviolet Spectrum
Atomic Oxygen 135.6 nm doublet
N2 LBH bands
Horizontal scan of disk & limb; image along vertical slit
• Temperature obtained on disk from rotational shape of N2 LBH bands
• O/N2 composition measured using ratio of 135.6 doublet to LBH bands
• Temperature on limb determined by slope of emission altitude profile
• O2 profile on limb from stellar occultations
• O+ at night observed using 135.6 recombination emission

## Slide 8: Modular Observing System Simulation Concept
MSIS-IRI
MSIS-IRI
TIE-GCM
TIE-GCM
TIE-GCM
GLOW
LBH VRB
LOS-RT
INSTR
MSIS-IRI
Analysis Algorithms
Fortran-90 / MPI
IDL / Bridge
Limb
Disk

## Slide 9: Observing System Simulation Concept — Models
Other Empirical
WACCM-X
TIME-GCM
TIE-GCM
MSIS-IRI

## Slide 10: TIE-GCM Simulations
E-region Electron Density (~110 km)
F-region Electron Density (~300 km)
Neutral Temperature (~160 km)
O/N2 Ratio (~160 km)

## Slide 11: Observing System Simulation Concept — Airglow
GLOW
Electron Transport
Neutral Atmos
Photo-electrons
Chemistry
Emissions
Solar Inputs
Auroral Inputs

## Slide 12: Observing System Simulation Concept — LBH Bands
LBH VRB

## Slide 13: Observing System Simulation Concept—Line-of-Sight
LOS-RT
Limb
Disk

## Slide 14: Line-of-Sight Integration
Satellite vector s

## Slide 15: CHIPSI Coordinates — Looking back from the Satellite
  c
  y
c, y are angles in east and north directions, relative to nadir
typical simulation grid ±10° at 0.1° resolution
a
a is the combined angle from the nadir vector

## Slide 16: Line-of-Sight Integration
Satellite vector s
r1
r2
v
a
Disk lines-of-sight intersect Earth

## Slide 17: Line-of-Sight Integration
Satellite vector s
r1
r2
rt
v
Limb lines-of-sight pass through atmosphere

## Slide 18: Line-of-Sight Integration
Satellite vector s
r1
r2
v
a
Disk lines-of-sight intersect Earth
|v| = |s| cos a ± (|r|2 – |s|2sin2a)1/2
subtract determinant if triangle is acute (pierce point case)
add determinant if triangle is oblique(limb exit case)
if determinant is zero, line-of-sight is tangent to r
if determinant is negative, line-of-sight misses atmosphere
r1
r2
rt
v
Limb lines-of-sight pass through atmosphere
Notes: Calculate line-of-sight direction from instrument angles
Calculate length of v1, v2
Transform to Cartesian coordinates
Calculate path through atmosphere and divide into segments
Integrate through airglow model, considering absorption along path
Build up observation cube at every angle and wavelength

## Slide 19: Airglow Simulations

## Slide 20: Image Cube Simulation
Disk Image Detector Image

## Slide 21: The December 2006 “AGU Storm”
O (5S) 135.6 nm doublet N2 LBH “short” (138–148 nm)

## Slide 22: Radiative Transfer Effects
Calculating the column brightness that emerges from the atmosphere is generally not as simple as just integrating along the line-of-sight.
If the emission is optically thin, then it is just the integral along the line-of-sight (except of course it’s really a cone, not a line, i.e., there is always some discrete field of view).
If the emission is partially absorbed, then absorption along path must be considered. That is easily done by calculating the column density and applying Beer’s Law.
If the emission is subject to scattering, particularly by resonant scattering, then things get interesting, because photons are added to the line-of-sight as well as removed.
N2 LBH bands are generally considered to only be absorbed by O2 (except perhaps for bands terminating in the v’’=0 ground state, which could be partially self-absorbed).
The O(5S) doublet at 135.6-135.9 nm is subject to absorption by O2 and weak resonant scattering. These effects are small but significant.
The O(3S) triplet at 130.2-130.4-130.6 nm is and allowed transition that is subject to very strong resonant scattering, including sunlight, and is extremely optically thick. This is of interest here primarily because it contributes to the instrumental background. That is also the case for the H Ly-a emission.

## Slide 23: Illustration of Multiple Scattering
e*
O
O
O
O2
hn (FUV)
N2
hn (EUV)
hn (FUV)
etc.
O

## Slide 24: Atomic Oxygen Transitions in the Far-Ultraviolet
Note that the “1356” oscillator strengths are orders of magnitude less than the “1304” oscillator strengths. Also note that the “1359” line is weaker than “1356,” and it doesn’t connect to the O(3P2) ground state.
Multiple scattering in the “1356” line is actually quite low, and virtually negligible in the 1359 line.
This suggests that we may approximate resonant scattering in the 1356 doublet using a simplified “monochromatic” approach, without having to consider frequency redistribution within the individual lines. That’s a good thing, because radiative transfer with frequency redistribution can be computationally intensive.

## Slide 25: Comparisons with GUVI Data using Gladstone Feautrier Code

## Slide 26: Comparison of Simplified Model to Gladstone Feautrier Code
Initial and final source functions, i.e., the amount of light produced per unit volume

## Slide 27: Comparison of Simplified Model to Gladstone Feautrier Code

## Slide 28: Comparison of Simplified Model to Gladstone Feautrier Code

## Slide 29: Latest & Greatest Simulations Applying all of the Above
O(5S) Doublet at 135.6 nm N2 LBH “short” bands 138-148 nm

## Slide 30: Conclusions
• We have a comprehensive observational simulation system for the GOLD mission.
• The methodology can be adapted to the ICON mission.
• The methodology can be adapted to other remote sensing observations as well.
• Based on community models; open-source code.
• Can use this system for algorithm development and data analysis.
• Still work to do:
  — Instrument simulator; WACCM-X and WAM interfaces; data assimilation...

## Slide 31: Backup on Coordinate Systems and Effective Temperature

## Slide 32: Coordinate Systems
• Earth Centered Inertial (ECI):
  z-axis is north pole of Earth
  x-axis is toward vernal equinox
  y-axis = z X x
• Earth Centered Rotational (ECR or ECEF):
  z-axis is north pole of Earth
  x-axis is intersect of prime meridian and equator
  y-axis = z X x
• Geographic (GEO):
  altitude relative to oblate ellipsoid surface
  longitude ±180° from prime meridian
  geodetic latitude:
    angle between local vertical and equator
• Instrument Coordinates (CHIPSI)
  c is angle from S/C nadir to east
  y is angle from S/C nadir to north
Earth Centered Rotational (ECR) coordinate system (a.k.a. Earth Centered Earth Fixed (ECEF), but this name is somewhat confusing, so ECR is preferred).

## Slide 33: Notes on Coordinate Systems
• ECI is largely unnecessary for geostationary observations of the Earth.
  — Probably will use ECI for stellar occultations, however
  — Approximations due to motion of vernal equinox and pole wobble
    — Typically surmounted by use of the J2000 reference frame
• ECR is the most straightforward coordinate system for line-of-sight calculations.
  — Particularly convenient for observations from geostationary orbit
  — ECR is used for the line-of-sight calculations described here
• ECR can be defined in either cartesian or spherical coordinates, but...
  — Note that polar angle q ≠ geodetic latitude
    — Angle from pole, not equator (similar to polar angle v. declination problem)
    — Defined in spherical coordinates, not on ellipsoid
• Models are in GEO coordinates, but ignore change in Earth radius.
  — However, we consider Earth radius when transforming from GEO to ECR
    — In essence, this warps the model onto the ellipsoid
    — Note that I am using the WGS-84 Ellipsoid, but not the EGM-96 harmonics
      — This results in an error of ~ ±0.1 km
• CHIPSI coordinates assume that the center of the detector is pointed at nadir.
  — May need to consider alignment and pointing offsets
  — S/C coordinate system for GOLD is x≈v; z toward nadir

## Slide 34: Altitude Profile of LBH Bands and Effective Temperature
Temperatures are obtained from N2 LBH bands that emit over a range of altitudes (~120~180 km in a nadir viewing geometry).
What the instrument obtains is an “Effective Temperature” over an altitude range:
where:
  h(s) is the emission contribution function:
    photons exiting atmosphere from each point along a line-of-sight
  B(c,y) = ∫ h(s) ds is the emergent brightness at specific observation angles (c,y).
Temperature variations can be analyzed in log-pressure coordinates instead of altitude coordinates in order to compensate for the weighting function ambiguity.
Validation can be performed using ground-based incoherent scatter radar observations of ion temperature, assuming that below ~200 km, Tn = Ti.
Need to consider the effects of solar activity, solar zenith angle, and observational zenith angle effects.

## Slide 35: Solar Activity Effect on LBH Bands
Altitude Coordinates
Log-Pressure Coordinates
F10.7 = 70: Teff = 578, zeff = 150 km, peff = 3.7 nb
F10.7 = 200: Teff = 843, zeff = 163 km, peff = 4.0 nb

## Slide 36: Solar Zenith Angle Effect on LBH Bands
Altitude Coordinates
Log-Pressure Coordinates
SZA = 0: Teff = 578, zeff = 150 km, peff = 3.7 nb
SZA = 70: Teff = 686, zeff = 162 km, peff = 2.1 nb

## Slide 37: Simulation of Effective Temperature