## Slide 1: Observation System Simulations for the GOLD Mission
Stan Solomon
High Altitude Observatory
National Center for Atmospheric Research
HAO/NCAR • 13 January 2016

## Slide 2: Outline
• The Global-scale Observations of the Limb and Disk mission
— introduction and overview
• Observations and measurement technique
• Global Modeling and airglow simulations
• Work in progress on radiative transfer effects

## Slide 3: Global UV Imaging: Primeval Heritage
John W. Young with Apollo 16 Far-Ultraviolet Camera
Far-Ultraviolet Image of the Earth George Carruthers, Instrument PI
Dayglow
Equatorial Ionization Anomalies
Aurora

## Slide 5: Global-scale Observations of the Limb and Disk
GOLD is an ultraviolet imaging spectrograph to measure the temperature, composition, and electron content of the terrestrial upper atmosphere from geostationary orbit.

## Slide 6: Global-scale Observations of the Limb and Disk
Richard Eastes, PI
UCF
Bill McClintock, DPI
CU/LASP
Alan Burns, Project Scientist
HAO/NCAR

## Slide 7: Benefits to Science and Society
  Advance Heliophysics science by linking solar observations to thermosphere-ionosphere physics
  Develop the next generation of upper-atmosphere models
  Address operational challenges in space-based communication, GPS navigation, and orbital tracking
Engage the public by providing near-real-time global images of aurora and space weather

## Slide 8: Scientific Objectives (official)
1. How do geomagnetic storms alter the temperature and composition structure of the thermosphere?
2. What is the global-scale response of the thermosphere to solar extreme-ultraviolet varability?
3. How significant are the effects of atmospheric waves and tides propagating from below on thermospheric temperature structure?
4. How does the nighttime equatorial ionosphere influence the formation and evolution of equatorial plasma density irregularities?

## Slide 9: Scientific Objectives (colloquial)
It seems axiomatic that the big-picture “synoptic” view will help us understand thermosphere-ionosphere dynamics, just as it has improved analysis of tropospheric weather.
Low-Earth Orbit observations have done a lot, but give us a solar-time-centric “asynoptic” view of the upper atmosphere.
Yet, GOLD is just one instrument, it can’t see everywhere all the time.
GOES-13
2012-10-28
1302 UTC

## Slide 10: TIE-GCM Simulations
E-region Electron Density (~110 km)
F-region Electron Density (~300 km)
Neutral Temperature (~160 km)
O/N2 Ratio (~160 km)

## Slide 11: TIE-GCM Simulations
E-region Electron Density (~110 km)
F-region Electron Density (~300 km)
Neutral Temperature (~160 km)
O/N2 Ratio (~160 km)

## Slide 12: GUVI Observations of O/N2 Composition Variations

## Slide 13: GOLD Ultraviolet Imaging Spectrograph
Instrument Summary | 
Volume | 51×55×69 cm3
Mass | 33 kg
Power | 53 W
Data Rate | 3.3 Mbit/sec
• Two identical channels
• Fully independent observing modes
  – Disk images and limb scans
    - Dayside: T and O/N2
    - Nightside: O+ density
  – Stellar occultation
• Heritage
    – Cassini UVIS
    – MESSENGER MASCS
    – MAVEN IUVS
  • Deployed on a Geostationary Comsat
    — Provided by SES-GS
    — Airbus SES-14 at 47.5 W long.
    — Launch in late 2017

## Slide 14: GOLD Ultraviolet Imaging Spectrograph
Alignment Cube
1-Shot Aperture Cover
Light Shade
Solar Safety Sensor
Telescope
Slit Mech
Aperture
Scan Mechanism
Scan Mirror Visor
Detector Electronics
HVPS
Detector Assembly
Collimating Mirror

## Slide 15: GOLD Measurement Technique
Daytime Far-Ultraviolet Spectrum
Atomic Oxygen 135.6 nm doublet
N2 LBH bands
Horizontal scan of disk & limb; image along vertical slit
• Temperature obtained on disk from rotational shape of N2 LBH bands
• O/N2 composition measured using ratio of 135.6 doublet to LBH bands
• Temperature on limb determined by slope of emission altitude profile
• O2 profile on limb from stellar occultations
• O+ at night observed using 135.6 recombination emission

## Slide 16: Modular Observing System Simulation Concept
MSIS-IRI
MSIS-IRI
TIE-GCM
TIE-GCM
TIE-GCM
GLOW
LBH VRB
LOS-RT
INSTR
MSIS-IRI
Analysis Algorithms
Parallel
Will be Parallel
Fast Enough
Serial OK
???
Fortran-90 / MPI
IDL / Bridge
Limb
Disk

## Slide 17: Observing System Simulation Concept — Models
Other Empirical
WACCM-X
TIME-GCM
TIE-GCM
MSIS-IRI

## Slide 18: Observing System Simulation Concept — Airglow
GLOW
Electron Transport
Neutral Atmos
Photo-electrons
Chemistry
Emissions
Solar Inputs
Auroral Inputs

## Slide 19: Observing System Simulation Concept — LBH Bands
LBH VRB

## Slide 20: Observing System Simulation Concept—Line-of-Sight
LOS-RT
Limb
Disk

## Slide 21: Observing System Simulation Concept — Instrument
INSTR
Limb
Disk

## Slide 22: Line-of-Sight Integration
Satellite vector s

## Slide 23: CHIPSI Coordinates — Looking back from the Satellite
  c
  y
c, y are angles in east and north directions, relative to nadir
typical simulation grid ±10° at 0.1° resolution
a
a is the combined angle from the nadir vector

## Slide 24: Line-of-Sight Integration
Satellite vector s
v
a

## Slide 25: Line-of-Sight Integration
Satellite vector s
r1
r2
v
a
Disk lines-of-sight intersect Earth

## Slide 26: Line-of-Sight Integration
Satellite vector s
r1
r2
rt
v
Limb lines-of-sight pass through atmosphere

## Slide 27: Line-of-Sight Integration
Satellite vector s
r1
r2
v
a
Disk lines-of-sight intersect Earth
r1
r2
rt
v
Limb lines-of-sight pass through atmosphere
|v| = |s| cos a ± (|r|2 – |s|2sin2a)1/2

## Slide 28: Line-of-Sight Integration
Satellite vector s
r1
r2
v
a
Disk lines-of-sight intersect Earth
|v| = |s| cos a ± (|r|2 – |s|2sin2a)1/2
subtract determinant if triangle is acute (pierce point case)
add determinant if triangle is oblique(limb exit case)
if determinant is zero, line-of-sight is tangent to r
if determinant is negative, line-of-sight misses atmosphere
r1
r2
rt
v
Limb lines-of-sight pass through atmosphere
Notes: Calculate line-of-sight direction from instrument angles
Calculate length of v1, v2
Transform to Cartesian coordinates
Calculate path through atmosphere and divide into segments
Integrate through airglow model, considering absorption along path
Build up observation cube at every angle and wavelength

## Slide 29: Airglow Simulations

## Slide 30: Image Cube Simulation
Disk Image Detector Image

## Slide 31: Image Cube Simulation
Disk Image Detector Image

## Slide 32: December Solstice Case
O (5S) 135.6 nm doublet N2 LBH “short” (138–148 nm)

## Slide 33: December Solstice Case
O(5S) / N2 LBH ratio

## Slide 34: The December 2006 “AGU Storm”
O (5S) 135.6 nm doublet N2 LBH “short” (138–148 nm)

## Slide 35: The December 2006 “AGU Storm”
O(5S) / N2 LBH ratio

## Slide 36: Radiative Transfer Effects
Calculating the column brightness that emerges from the atmosphere is generally not as simple as just integrating along the line-of-sight.
If the emission is optically thin, then it is just the integral along the line-of-sight (except of course it’s really a cone, not a line, i.e., there is always some discrete field of view).
If the emission is partially absorbed, then absorption along path must be considered. That is easily done by calculating the column density and applying Beer’s Law.
If the emission is subject to scattering, particularly by resonant scattering, then things get interesting, because photons are added to the line-of-sight as well as removed.
N2 LBH bands are generally considered to only be absorbed by O2 (except perhaps for bands terminating in the v’’=0 ground state, which could be partially self-absorbed).
The O(5S) doublet at 135.6-135.9 nm is subject to absorption by O2 and weak resonant scattering. These effects are small but significant.
The O(3S) triplet at 130.2-130.4-130.6 nm is and allowed transition that is subject to very strong resonant scattering, including sunlight, and is extremely optically thick. This is of interest here primarily because it contributes to the instrumental background. That is also the case for the H Ly-a emission.

## Slide 37: Illustration of Multiple Scattering
e*
O
O
O
O2
hn (FUV)
N2
hn (EUV)
hn (FUV)
etc.
O

## Slide 38: Atomic Oxygen Transitions in the Far-Ultraviolet
Note that the “1356” oscillator strengths are orders of magnitude less than the “1304” oscillator strengths. Also note that the “1359” line is weaker than “1356,” and it doesn’t connect to the O(3P2) ground state.
Multiple scattering in the “1356” line is actually quite low, and virtually negligible in the 1359 line.
This suggests that we may approximate resonant scattering in the 1356 doublet using a simplified “monochromatic” approach, without having to consider frequency redistribution within the individual lines. That’s a good thing, because radiative transfer with frequency redistribution can be computationally intensive.

## Slide 39: Comparisons with GUVI Data using Gladstone Feautrier Code

## Slide 40: Comparison of Simplified Model to Gladstone Feautrier Code
Initial and final source functions, i.e., the amount of light produced per unit volume

## Slide 41: Comparison of Simplified Model to Gladstone Feautrier Code

## Slide 42: Comparison of Simplified Model to Gladstone Feautrier Code

## Slide 43: Latest & Greatest Simulations Applying all of the Above
O(5S) Doublet at 135.6 nm N2 LBH “short” bands 138-148 nm

## Slide 44: Conclusions
• We have a comprehensive observational simulation system for the GOLD mission.
• The methodology can be adapted to the ICON mission.
• The methodology can be adapted to other remote sensing observations as well.
• Based on community models; open-source code.
• Can use this system for algorithm development and data analysis.
• Still work to do:
  — Oi 130.4 nm triplet; instrument simulator; WACCM-X and WAM interfaces; data assimilation...

## Slide 45: Backup on Viewing Geometry and Coordinate Systems

## Slide 46: Coordinate Systems
• Earth Centered Inertial (ECI):
  z-axis is north pole of Earth
  x-axis is toward vernal equinox
  y-axis = z X x
• Earth Centered Rotational (ECR or ECEF):
  z-axis is north pole of Earth
  x-axis is intersect of prime meridian and equator
  y-axis = z X x
• Geographic (GEO):
  altitude relative to oblate ellipsoid surface
  longitude ±180° from prime meridian
  geodetic latitude:
    angle between local vertical and equator
• Instrument Coordinates (CHIPSI)
  c is angle from S/C nadir to east
  y is angle from S/C nadir to north
Earth Centered Rotational (ECR) coordinate system (a.k.a. Earth Centered Earth Fixed (ECEF), but this name is somewhat confusing, so ECR is preferred).

## Slide 47: Notes on Coordinate Systems
• ECI is largely unnecessary for geostationary observations.
  —Approximations due to motion of vernal equinox and pole wobble
    — Typically surmounted by use of J2000 reference frame
• ECR is the most straightforward coordinate system for line-of-sight calculations.
• ECR can be defined in either cartesian or spherical coordinates, but...
  — Note that polar angle q ≠ geodetic latitude
    — Angle from pole, not equator (similar to polar angle v. declination problem)
    — Defined in spherical coordinates, not on ellipsoid
• Models are in GEO coordinates, but ignore change in Earth radius.
  — However, we consider Earth radius when transforming from GEO to ECR
    — In essence, this warps the model onto the ellipsoid
    — Note that I am using the WGS-84 Ellipsoid, but not the EGM-96 harmonics
      — This results in an error of ~ ±0.1 km
• CHIPSI coordinates assume that the center of the detector is pointed at nadir.
  — May need to consider alignment and pointing offsets
  — S/C coordinate system for GOLD is x≈v; z toward nadir